## Slide 1: Design, Build and Test a Small Office Network
CCNA 1 Group Practical Lab 1 · Uganda Christian University
Group X: add member names and roles
Notes: Introduce the group: names and roles (designer/documenter, switch engineer, router engineer, tester/troubleshooter). Say that the network, not the slides, is the evidence: we will demonstrate live in Packet Tracer. Total time about 25 minutes plus 10 minutes of questions.

## Slide 2: The Kampala Small Office needs a network
The ICT Directorate gave us one block, 192.168.10.0/24, one router, three switches and UTP cabling.
50
Administration
LAN 1 · future hosts
25
Operations
LAN 2 · future hosts
10
IT and Servers
LAN 3 · future hosts
What the network must do
Every device reaches every other, in the same LAN and across LANs
Correct cables, addresses, masks and gateways
Secured: passwords, banner, SSH, unused ports shut
Intranet page opens by name: http://intranet.office.local
IPv6 dual stack for the future
Documented so another technician can rebuild it
Notes: Part 1 of the presentation, about 2 minutes. State what the office needs: three working areas, one address block, one router, three switches. Mention the requirements: communication across LANs, correct cabling and addressing, secure management, a web page by name, IPv6 dual stack, and full documentation.

## Slide 3: Design: three LANs joined by one router
R-OFFICE
gateways .1 · .65 · .97
SW-ADMIN .2
PC-ADM1
.10
PC-ADM2
.11
Printer-ADM
.20
LAN 1 Admin · 192.168.10.0/26
SW-OPS .66
PC-OPS1
.70
PC-OPS2
.71
Laptop-OPS
.72
LAN 2 Operations · 192.168.10.64/27
SW-IT .98
Server-IT
.100
PC-IT1
.101
PC-IT2
.102
LAN 3 IT · 192.168.10.96/28
All 12 links are straight-through UTP · switch uplinks use Gi0/1 · hosts use Fa0/1 to Fa0/3 · host addresses are 192.168.10.x
Notes: Part 2, about 3 minutes (shared with the subnet and addressing slides). Walk through the topology top-down: end devices, access switches, router as default gateway. All 12 links are straight-through. Router G0/0, G0/1, G0/2 go to Gi0/1 of SW-ADMIN, SW-OPS and SW-IT.

## Slide 4: Subnetting: VLSM from one /24
LAN | Hosts | Prefix and mask | Network | Usable range | Broadcast
LAN 1 Admin | 50 | /26 · 255.255.255.192 | 192.168.10.0 | 192.168.10.1 – .62 | 192.168.10.63
LAN 2 Ops | 25 | /27 · 255.255.255.224 | 192.168.10.64 | 192.168.10.65 – .94 | 192.168.10.95
LAN 3 IT | 10 | /28 · 255.255.255.240 | 192.168.10.96 | 192.168.10.97 – .110 | 192.168.10.111
How we sized each block
Smallest h where 2^h − 2 ≥ hosts. Example: 50 hosts need h = 6, so 62 usable and a /26.
Room to grow
192.168.10.112 to 192.168.10.255 stays unused, reserved for future LANs. No addresses are wasted.
Notes: Part 2. Explain VLSM: allocate the largest network first, start each block right after the previous broadcast address. 50 hosts need 6 host bits (2^6 - 2 = 62) so /26; 25 hosts need 5 bits so /27; 10 hosts need 4 bits so /28. Free space 192.168.10.112 to .255 is kept for growth. Be ready to calculate any subnet live.

## Slide 5: Addressing plan: IPv4 and IPv6 dual stack
Device | IPv4 (192.168.10.x) | Prefix | Gateway | IPv6 (2001:DB8:ACAD:…)
R-OFFICE G0/0 · G0/1 · G0/2 | .1 · .65 · .97 | /26 · /27 · /28 | n/a | 10::1 · 20::1 · 30::1
SW-ADMIN · SW-OPS · SW-IT (VLAN 1) | .2 · .66 · .98 | /26 · /27 · /28 | .1 · .65 · .97 | n/a
PC-ADM1, PC-ADM2, Printer-ADM | .10 · .11 · .20 | /26 | .1 | 10::10 · 10::11
PC-OPS1, PC-OPS2, Laptop-OPS | .70 · .71 · .72 | /27 | .65 | 20::70 · ::71 · ::72
Server-IT, PC-IT1, PC-IT2 | .100 · .101 · .102 | /28 | .97 | 30::100 · ::101 · ::102
DNS server for every device: 192.168.10.100 (Server-IT) · domain office.local · static addressing everywhere
Notes: Part 2. Show the addressing table. Hosts are numbered so that the last octet tells the department: 10s Admin, 70s Operations, 100s IT. Each LAN has its own mask and gateway. The router uses FE80::1 as link-local on all three interfaces. DNS for every device is Server-IT at 192.168.10.100.

## Slide 6: Build: devices, cables, end devices
13
devices: 1 router, 3 switches, 9 end devices
12
straight-through cables
3
LANs, three different masks
2
services: DNS and HTTP
Physical build
Router 2911, switches 2960-24TT
Ports follow the port map exactly
End-device links green; router links red until no shutdown
End devices
Static IP, mask, gateway and DNS 192.168.10.100
Verified with ipconfig /all
Before the router: same-LAN ping works, cross-LAN fails
Notes: Part 3, about 3 minutes. Cabling: we chose every cable ourselves, no automatic cable. Link lights: end-device links go green; router links stay red until no shutdown. End devices: IP, mask, gateway and DNS entered by hand, verified with ipconfig /all. Before the router was configured, same-LAN pings worked and cross-LAN pings failed.

## Slide 7: Switches: identity, access, management
Identity: hostname, no ip domain-lookup
Access: enable secret, console and VTY passwords
service password-encryption and login banner
Management: SVI on VLAN 1 plus default gateway
Port descriptions on every used port
Saved with copy running-config startup-config
hostname SW-ADMIN
enable secret ********
service password-encryption
interface vlan 1
ip address 192.168.10.2 255.255.255.192
no shutdown
ip default-gateway 192.168.10.1
Verify live
show ip interface brief
show mac address-table
show running-config
Notes: Part 4, about 4 minutes (switches and router). Show the saved configuration and the key verification commands. Explain why the SVI needs ip default-gateway (remote management from another LAN). Show show mac address-table after a ping to prove the switch learns source MAC addresses. Do not read passwords aloud; they are lab-only.

## Slide 8: Router: the gateway for all three LANs
interface gigabitEthernet 0/0
ip address 192.168.10.1 255.255.255.192
no shutdown
interface gigabitEthernet 0/1
ip address 192.168.10.65 255.255.255.224
no shutdown
interface gigabitEthernet 0/2
ip address 192.168.10.97 255.255.255.240
no shutdown
Interfaces start shut down. no shutdown turns the red links green, and show ip interface brief must say up/up.
Code | Route | Via
C | 192.168.10.0/26 | G0/0
C | 192.168.10.64/27 | G0/1
C | 192.168.10.96/28 | G0/2
C is connected; L is the router's own /32 address
No gateway of last resort: no Internet in this lab
Server .100 matches 192.168.10.96/28, the longest prefix
Notes: Part 4. Router interfaces are shut down by default; no shutdown brings them up. Each interface address is the default gateway of its LAN. Explain the routing table: C is a connected network, L is the router's own /32 address. The table says variably subnetted, 6 subnets, 3 masks. No gateway of last resort because there is no Internet in this lab. A packet for 192.168.10.100 matches 192.168.10.96/28 by longest prefix match.

## Slide 9: Live demo: across LANs and over IPv6
On PC-ADM1
ping 192.168.10.1
ping 192.168.10.65
ping 192.168.10.97
ping 192.168.10.100
tracert 192.168.10.100
ping 2001:db8:acad:30::100
Across LANs: all pings succeed; the first may lose one reply (ARP)
tracert: hop 1 is 192.168.10.1 (gateway), hop 2 is 192.168.10.100
TTL: 128 inside a LAN, 127 after one router hop
IPv6: needs ipv6 unicast-routing; IPv4 stays untouched
Notes: Part 5, about 3 minutes. Run these on PC-ADM1 live. Point out that the first ping may lose one reply because of ARP. In tracert, hop 1 is the default gateway and hop 2 the server. TTL 128 inside the LAN becomes 127 after crossing the router. For IPv6, ipv6 unicast-routing must be on; without it the router does not forward IPv6 packets.

## Slide 10: Services and protocols in action
1
DNS
Query to Server-IT on UDP port 53; answer is the A record 192.168.10.100
2
ARP
Broadcast asks for the gateway MAC; the unicast reply is cached
3
TCP
Three-way handshake: SYN, SYN-ACK, ACK to destination port 80
4
HTTP
GET request, 200 OK with the page, then FIN closes the connection
Demo. Open http://intranet.office.local on PC-OPS1 and step through the events in Simulation mode.
Key point. IP addresses stay the same end to end. MAC addresses change at every router hop.
Notes: Part 6, about 4 minutes. Server-IT runs HTTP and DNS (records intranet.office.local and printer.office.local). Demo: open http://intranet.office.local from PC-OPS1 in Simulation mode and step through. Show one ARP exchange and one TCP three-way handshake. Key conclusion: IP addresses stay the same end to end, MAC addresses change at every router hop, and TTL drops by 1 at each router. Switch back to Realtime mode afterwards.

## Slide 11: Security: SSH, port security, unused ports
1
SSH, not Telnet
Telnet sends passwords in clear text
Domain name, RSA 2048, SSH version 2
transport input ssh, login local
Telnet is now refused
2
Port security
Sticky MAC, maximum 1 per port
Violation mode: shutdown
Demo: swap two PC cables, ports go err-disabled
Recover: shutdown, then no shutdown
3
Unused ports shut
Fa0/4 to Fa0/24 and Gi0/2 on every switch
Described as UNUSED
Uplink Gi0/1 stays up
Checked with show interfaces status
Evidence: a security checklist for every device, and every configuration saved to NVRAM
Notes: Part 7, about 3 minutes. Demo: ssh -l netadmin 192.168.10.66 from PC-ADM1 (works from another LAN because the switch has a default gateway), then telnet 192.168.10.2 is refused. Port security: swap the cables of PC-ADM1 and PC-ADM2, ports go err-disabled; recover with shutdown then no shutdown. Show show interfaces status to prove unused ports are disabled and the uplink Gi0/1 is still connected.

## Slide 12: Troubleshooting with a four-step ticket
1 Problem
2 Diagnosis
3 Solution
4 Verification
Example ticket: wrong gateway
Problem: PC-IT1 reaches its own LAN, nothing else
Diagnosis: ipconfig shows gateway 192.168.10.65; ping to it fails
Solution: set gateway 192.168.10.97
Verification: ping Server-IT and PC-OPS1, re-run test plan
Where the ping stops | Likely cause
Cannot ping the gateway | Wrong gateway or mask, router interface down
Gateway works, other LAN fails | Router, destination or its mask
IP works, name fails | DNS address or DNS records
Red link light | Cable type, port, shutdown, power
Notes: Part 8, about 3 minutes. Fix a fault introduced by the other group or the lecturer using the four-step ticket: Problem, Diagnosis, Solution, Verification. Method: define the problem exactly, gather facts, make one hypothesis, change one thing at a time, verify from the user side, document. The example ticket is the wrong default gateway on PC-IT1.

## Slide 13: The packet journey: PC-OPS1 to the intranet
1
DNS query
UDP port 53 to 192.168.10.100. 70 AND /27 = 64 but the server is in 96, so it is remote: use the gateway
2
ARP for the gateway
Broadcast asks who has 192.168.10.65. The router replies and the MAC is cached
3
Frame to the router
Source MAC PC-OPS1, destination MAC R-OFFICE G0/1; IPs .70 to .100; the switch forwards by its MAC table
4
Routing
Longest match 192.168.10.96/28 via G0/2, TTL minus 1, ARP for the server, new frame with the same IPs
5
TCP handshake
SYN, SYN-ACK, ACK from a random source port to destination port 80
6
HTTP response
GET, then 200 OK with the page, ACKs and FIN. Bits travel as signals on UTP
Notes: Part 9, the Packet Journey Challenge. Be ready for the lecturer to pick any source and destination. AND check for stage 1: 70 = 01000110 AND 11100000 = 01000000 = 64, the server 100 = 01100100 AND 11100000 = 01100000 = 96, so the DNS server is remote and the PC sends to its gateway. Use the words encapsulation, PDU, MAC address, IP address, port number, ARP, default gateway, routing table, TTL, broadcast, unicast, DNS, TCP, UDP and HTTP.

## Slide 14: Questions?
Planned, built, secured, tested and documented.
IP addresses stay the same end to end; MAC addresses change at every router hop.
Notes: Part 9, about 10 minutes of questions. Every member must be able to explain the whole network: the lecturer chooses who answers. Likely topics: subnet calculation by hand, the AND operation, MAC and IP changes at each hop, ARP, TCP versus UDP, SSH versus Telnet, port security modes, and how to reset a device.